## Slide 1
Presidency
School of Computer Science and Engineering
Mini Project (CSE7102)
REVIEW-2 PRESENTATION
Date: 26-09-2026

## Slide 2: Development of a Software Application for Analysis and Processing of DVB-S2 Receiver Output Stream
Project ID: PRJ_111 | Course: CSE7102 - Mini Project | Review-2 (26-09-2026)
Program Name: | B.Tech Computer Science & Engineering
Course & Code: | CSE7102 - Mini Project
Review Milestone: | Review-2 (26-09-2026)
HoD Name: | Head of Department, CSE
Program Coordinator: | Dr. Irfan Rajab Bhat
School Coordinator: | Mr. Muthuraju V
Under the Supervision of:
Irfan Rajab Bhat
Assistant Professor Department of Computer Science and Engineering Presidency University, Bengaluru
CSS7102- Mini Project Review-2
Program: B.Tech Computer Science and Engineering
HoD: Dr. T.V. Rajinikanth / Head of Department
Program Project Coordinator: Dr. Irfan Rajab Bhat
School Project Coordinator: Mr. Muthuraju V
No. | Team Member Name | University Roll No.
1 | Sk Samad | 20231COM0031
2 | Y Vengala Rao | 20231COM0001
3 | C Rakeshwar | 20231COM0008
Group members details:
Panel No: Panel 11 / PRJ_111

## Slide 3: INDEX / TABLE OF CONTENTS
Project Fundamentals & Architecture
01. Problem Statement: Multi-format DVB-S2 stream challenges
02. Objectives: 3–5 measurable project goals
03. Literature Review: DVB-S2, GSE & anomaly detection research
04. Research Gap: Unifying post-demodulation stream diagnostics
05. Proposed Methodology: 5-layer modular alternative-format architecture
06. System Architecture: End-to-end data pipeline flow
07. Workflow & Data Strategy: Multi-dataset ingestion across 5 raw folders
08. Seven Core Features: Overview of F1 through F7 modules
Implementation & Verification Results
09. Feature F1: Stream Health & Priority-1 checks
10. Feature F2: AI Anomaly Detection via Isolation Forest
11. Feature F3: Pattern Detection & Shannon Entropy
12. Feature F4: Spatial Activity Timeline & HTML Dashboards
13. Feature F5: Diagnostic Anomaly Explanations (Signed Z-Score)
14. Feature F6: Stream Comparison Engine & Semantic Audit
15. Feature F7: Automatic Multi-Format Diagnostic Reporting
16. Validation & Results: 240/240 Tests passing, Ground Truth Ledger, GitHub & Roadmap

## Slide 4: PROBLEM STATEMENT
Format Heterogeneity: DVB-S2 receiver output streams exist across multiple alternative encapsulation layers (Baseband Frames, GSE packets, and MPEG Transport Streams), requiring fragmented, proprietary command-line utilities for inspection.
Lack of Intelligent Anomaly Detection: Conventional stream analyzers rely on basic static threshold checks, failing to detect subtle temporal anomalies, sudden jitter variations, corrupted modulation frames, or unexpected multiplex behaviors.
Absence of Unified Diagnostic Platforms: Existing open-source tools typically focus only on one isolated format (e.g., MPEG-TS only or PCAP inspection only) without providing unified health metrics, explainable AI diagnostics, comparative stream analysis, or automated report generation.
Need for Unified Software Workflow: An urgent operational requirement exists for an integrated software application capable of parsing all three native formats, evaluating stream integrity, detecting statistical anomalies, and delivering root-cause diagnostic explanations rather than raw packet dumps.

## Slide 5: PROJECT OBJECTIVES
1. Multi-Format Receiver Stream Ingestion: Ingest and parse native DVB-S2 receiver output streams across three alternative formats: Baseband (BB) Frames, GSE frames, and MPEG Transport Streams (TS).
2. Stream Health & Integrity Assessment: Compute quantitative stream integrity indicators including packet loss rate, Continuity Counter (CC) error frequency, sync byte validation, and jitter.
3. Machine Learning Anomaly Detection: Deploy calibrated unsupervised machine learning algorithms (Isolation Forest with sigmoid score normalization) to identify irregular stream behavior and transmission degradation.
4. Structural Pattern & Entropy Mining: Discover recurring patterns in stream transmission, PID multiplex allocations, modal Data Field Lengths (DFL), and Shannon entropy dynamics.
5. Interactive Visualization & Explainable Diagnostics: Deliver dynamic spatial activity timelines, bounded signed Z-score feature attributions, differential stream comparisons, and automated multi-format diagnostic reports.

## Slide 6: LITERATURE / RESEARCH UNDERSTANDING
DVB-S2 Standard Architecture (Morello & Mignone, 2006): Pioneered the second-generation satellite broadcasting architecture (ETSI EN 302 307), defining physical/link framing, MODCOD adaptation, BBHeader structure, and CRC-8 integrity.
Adaptive Coding & GSE Encapsulation (Albertazzi 2005, Cantillo 2007/2008): Investigated Adaptive Coding and Modulation (ACM) and Generic Stream Encapsulation (ETSI TS 102 606) for efficient IP transport over DVB-S2 continuous generic streams.
Satellite Telemetry Anomaly Detection (Arbon 2018, Pan 2020, Hundman 2018): Evaluated unsupervised tree-based models and LSTM networks for spacecraft telemetry, establishing that tree ensembles achieve robust anomaly detection without catastrophic deep-learning false positives.
Explainable AI & Diagnostic Attribution (Zeng 2022, Wang 2023): Demonstrated feature-attention mechanisms and causal attribution for interpreting telemetry deviations, reinforcing the need for interpretable Z-score feature attributions in stream diagnostics.

## Slide 7: RESEARCH GAP ADDRESSED BY PRJ_111
Limitations of Existing Tools
Protocol Inspection (Wireshark/TSDuck): Manual packet inspection tools lack automated ML anomaly detection, timeline tracking, and executive report compilation.
Physical RF Signal Research: Focuses strictly on raw I/Q samples and modulation recognition (QPSK/8PSK), operating below the de-encapsulated digital stream layer.
Generic Network NIDS: Designed for IP Ethernet traffic; unsuited for native DVB-S2 link framing (BBHeaders, GSE fragmentation, MPEG-TS PIDs).
PRJ_111 Engineering Solution
Multi-Format Integration: First unified framework accepting BBFrame, GSE, and MPEG-TS post-demodulation streams.
Automated ML Anomaly Detection: Calibrated Isolation Forest with sigmoid normalization and rolling spatial windowing.
Semantic Cross-Format Audit: Strictly guards metric comparability to prevent invalid cross-format conclusions.
Automated Tripartite Reporting: Compiles executive reports in JSON, Markdown, Plain Text, and offline HTML5.

## Slide 8: PROPOSED METHODOLOGY & ARCHITECTURE
Foundational Architectural Principle: Baseband Frames (BBFrame), Generic Stream Encapsulation (GSE), and MPEG Transport Stream (TS) are treated as native alternative receiver output formats, NOT a mandatory sequential conversion pipeline (BBFrame → GSE → TS).
1. Ingestion Layer: Multi-tier magic-byte & heuristic format sniffer automatically dispatches incoming streams to dedicated native parsers.
2. Parsing & Preprocessing Layer: Robust binary parsers extract 188B TS packets, variable GSE PDUs, and 10B BBHeaders with table-driven CRC-8 verification.
3. Feature Extraction Layer: Standardized feature extractor constructs CommonMetrics and format-specific telemetry without cross-format flattening.
4. Intelligent Analysis Engine: Houses F1 Health Engine, F2 Isolation Forest, F3 Pattern Detector, and F5 Signed Z-Score Diagnostic Explainer.
5. Application & Reporting Layer: Houses F4 Spatial Offset Timelines, F6 Stream Comparison Engine, and F7 Executive Diagnostic Report Generator.

## Slide 9: SYSTEM ARCHITECTURE DIAGRAM
Layer 1: Stream Ingestion: Native receiver captures (.ts, .pcap, .bin) ingested with automatic format sniffing.
Layer 2: Format Parsers: Dedicated parsers for MPEG-TS, GSE PDUs, and DVB-S2 BBFrames with table CRC-8.
Layer 3: Unified Features: Extracts CommonMetrics and format-specific structural metrics.
Layer 4: AI & Diagnostics: F1 Health scoring, F2 Isolation Forest anomaly detection, F3 Pattern/Entropy mining, F5 Z-score explainer.
Layer 5: Application Output: F4 Timelines, F6 Semantic Comparisons, and F7 Executive Reports.
Figure 1: PRJ_111 Layered System Architecture & Data Flow Pipeline

## Slide 10: END-TO-END PROCESSING PIPELINE
Step 1: Stream Ingestion & Sniffing: StreamHandler inspects binary headers to auto-detect stream type and dispatches to TSParser, GSEParser, or BBFrameParser.
Step 2: Deterministic Binary Parsing: Parses framing headers, checks sync byte 0x47, validates CC sequence, extracts GSE PDUs, or checks BBHeader CRC-8.
Step 3: Feature Extraction & Windowing: Calculates payload byte volumes, error counts, and aggregates stream telemetry into rolling spatial windowing blocks.
Step 4: AI Anomaly & Pattern Mining: Executes F1 Priority-1 health scoring, F2 Isolation Forest inference, F3 Shannon entropy calculation, and F5 Z-score attribution.
Step 5: Differential Audit & Report Synthesis: Executes F6 semantic cross-format audit and F7 multi-renderer executive report generation (JSON/MD/TXT/HTML).

## Slide 11: DATASET STRATEGY & RECEIVER OUTPUT FORMATS
01_BBFRAME_GSE/ (BBFrame Dataset): dvb-s2_bb_example.pcap (2.35 MB, 4,309 BBFrames) — Real DVB-S2 Baseband validation capture for link-layer header analysis.
02_GSE/ (GSE Dataset): GSExtract/sample.ts (9,324 B, 14 PDUs) — Real GSE encapsulation validation capture for IP PDU de-encapsulation.
03_TS/ (MPEG-TS Dataset): DVBS2_toolkit/sample.ts (3.42 MB, 18,176 pkts) + Astra 19.2°E satellite captures — Real MPEG-TS transport stream validation data.
04_RFI_AI/ & 05_REAL_DVB_S2/ (Reference Archives): Blockstream over-the-air DVB-S2 capture (blockstream.ts & ip_packets.pcap) + RFI reference data archives for AI feature exploration.
Data Retention & Security Policy: All raw binary datasets are retained locally on dev workstations and excluded from GitHub via .gitignore adhering to best practices.

## Slide 12: SEVEN CORE TARGET FEATURES (F1–F7)
Core Analytical Engines (F1–F4)
F1: Stream Health Analysis: Quantifies transmission quality via ETSI TR 101 290 Priority-1 checks and 0–100 health scoring.
F2: AI Anomaly Detection: Unsupervised Isolation Forest (c=0.05) flagging atypical stream deviations with sigmoid normalization.
F3: Pattern Detection: Identifies recurring PID shares, modal DFL sizing, protocol distributions, and Shannon entropy.
F4: Spatial Activity Timeline: Visualizes stream activity, bandwidth consumption, and error events over physical byte offsets.
Diagnostic & Reporting Engines (F5–F7)
F5: Anomaly Explanation: Delivers bounded signed Z-score attributions mapping deviations to physical subsystems.
F6: Stream Comparison Engine: Side-by-side differential analysis enforcing a semantic audit to prevent invalid cross-format metric comparison.
F7: Automatic Analysis Report: Generates consolidated executive diagnostic reports across JSON, Markdown, Plain Text, and offline HTML5.

## Slide 13
F1 — STREAM HEALTH AND PRIORITY-1 CHECKS
Priority-1 Stream Integrity Checks: Evaluates ETSI TR 101 290 Priority-1 indicators: MPEG-TS sync byte consistency (0x47), Continuity Counter (CC) errors, Transport Error Indicator (TEI) flags, and BBHeader CRC-8 checks.
Objective Health Scoring Equation: S_health = 100.0 - sum(penalties), strictly bounded within [0.0, 100.0]. Classifies streams into HEALTHY [90-100], DEGRADED [60-89], or CRITICAL [0-59].
Empirical Baseline Validation: All real-world validation captures (sample.ts, dvb-s2_bb_example.pcap, GSExtract/sample.ts) achieved 100.00 / 100 (HEALTHY) with zero framing errors.
Controlled Fault Injection: Synthetic error injection verified that CC sequence breaks, sync byte corruption, and CRC-8 failures cleanly trigger objective health score penalties.

## Slide 14: F2 — AI-BASED ANOMALY DETECTION
Algorithm & Configuration: Unsupervised Isolation Forest ensemble (contamination factor c=0.05, format-specific rolling windowing).
Sigmoid Score Normalization: Raw tree decision scores mapped to [0.0, 1.0]: S_norm = 1 / (1 + e^-k(s_raw - theta)).
MPEG-TS Anomaly Results: 91 windows (w=200 pkts): 5 anomalous windows [1, 2, 12, 88, 90], Peak Score = 0.8576 (EOF boundary).
BBFrame Anomaly Results: 87 windows (w=50 frames): 5 anomalous windows [0, 83, 84, 85, 86], Peak Score = 0.7406 (EOF boundary).
GSE Anomaly Results: 5 windows (w=3 PDUs): 1 anomalous window [4], Peak Score = 0.5018 (EOF boundary).
Figure 2: F2 Interactive Anomaly Detection Interface & Score Trajectory

## Slide 15: F3 — PATTERN DETECTION & SHANNON ENTROPY
Operational Behavior Profiling: Tracks multiplex allocations, modal sizing, protocol shares, and structural transitions over rolling windows.
Shannon Entropy Calculation: H(X) = -sum(P(x_i) * log2(P(x_i))) measures information uncertainty and multiplex randomness.
MPEG-TS Dominant PID & Entropy: Dominant PID 256 (98.5% multiplex share), Shannon entropy = 0.1361 bits (highly concentrated video broadcast multiplex).
GSE Protocol Distribution: Dominant protocol GSE_EXT_NPA (100.0% share), Shannon entropy = 0.0000 bits (single-protocol transport stream).
BBFrame Modal Sizing: Modal Data Field Length (DFL) = 8304 bits (92.0% share), reflecting uniform physical frame packaging.

## Slide 16: F4 — SPATIAL ACTIVITY TIMELINE
Physical Offset Indexing: Indexes stream activity over physical byte offsets and sequential unit indices, avoiding wall-clock clock fabrication.
Time-Series Metric Extraction: Continuously tracks rolling health score, anomaly score trajectory, and payload byte density.
Event Mapping Engine: Automatically flags health drops, anomaly peaks, and structural transitions on the spatial axis.
Standalone Interactive Dashboard: Compiles self-contained HTML5 dashboards with embedded CSS for responsive offline operator inspection.
Figure 3: F4 Spatial Activity Timeline Dashboard

## Slide 17: F5 — DIAGNOSTIC ANOMALY EXPLANATIONS
Explainable AI Mechanism: Computes bounded signed Z-scores: Z_i = (x_i - mu_i) / max(sigma_i, sigma_min), capped at [-20.0, +20.0].
Physical Subsystem Mapping: Maps deviated feature Z-scores directly to physical satellite stream subsystems:
• dominant_pid: MPEG-TS Multiplex / Dominant PID Allocation
• null_packet_ratio: Bandwidth Adaptation / Null Stuffing
• crc_error_count: Baseband Header Integrity / CRC Checksum
• modal_dfl_bits: Frame Sizing / Mode Adaptation
Ranked Diagnostic Synthesis: Ranks features by |Z| and generates evidence-grounded explanatory sentences for operators.

## Slide 18: F6 — STREAM COMPARISON & SEMANTIC AUDIT
Semantic Cross-Format Audit: Enforces strict metric compatibility guard: 9 metrics barred cross-format (total_units, valid_units, mean_payload, etc.).
Cross-Format Comparable Metrics: Only total_payload_bytes and integrity_ratio are physically comparable across distinct formats.
MPEG-TS vs BBFrame Payload: MPEG-TS payload = 3,267,305 B, BBFrame payload = 1,958,826 B. Delta = -1,308,479 B (-40.05% SUBSTANTIAL shift).
Integrity Ratio Comparison: MPEG-TS integrity = 1.0000, BBFrame integrity = 1.0000 (EQUAL, perfect syntactic integrity across both captures).
Figure 4: F6 Stream Comparison Interface & Differential Metrics

## Slide 19: F7 — AUTOMATIC MULTI-FORMAT REPORTING
Non-Duplication Executive Synthesis: Directly consumes outputs from F1–F6 without re-parsing streams or re-running ML models.
Tripartite Findings Taxonomy: Categorizes every report finding into three epistemological registers: OBSERVED_FACT, STATISTICAL_FINDING, and ENGINEERING_INTERPRETATION.
Multi-Format Renderers: Exports comprehensive diagnostic reports in structured JSON, GitHub-Flavored Markdown, CP-1252-safe Plain Text, and offline HTML5.
Domain-Safety Guard: Immutable guard blocks speculative physical RF/hardware claims in generated report text.
Figure 5: F7 Executive Diagnostic Report Generator Interface

## Slide 20: SYSTEM IMPLEMENTATION PROGRESS
Current Project Completion Status: Core implementation is substantially completed across F1–F7, with automated validation and demonstration outputs available. Backend features F1 through F7 are 100% implemented, audited, and frozen.
Stream Ingestion & Sniffing: 100% Completed & Audited (Multi-tier format sniffer, 14 dedicated unit tests passing).
Multi-Format Parsers (TS / GSE / BBFrame): 100% Completed & Audited (61 dedicated unit tests passing, table-driven CRC-8 implemented).
Analytics & AI Engines (F1–F7): 100% Completed & Audited (132 dedicated unit tests passing across health, anomaly, timeline, explanation, comparison, and reporting).
Automated Test Suite: 100% Completed & Verified (240/240 tests passing across backend and frontend).

## Slide 21: AUTHORITATIVE GROUND TRUTH RESULTS LEDGER
Metric Dimension | MPEG-TS Stream | BBFrame Stream | GSE Stream | Cross-Format Comparison
Input File Path | sample.ts | dvb-s2_bb_example.pcap | GSExtract/sample.ts | MPEG-TS vs BBFrame
Total Units Parsed | 18,176 packets | 4,309 frames | 14 PDUs | 18,176 pkts vs 4,309 frames
Syntactic Validity | 100.0% (18,176/18,176) | 100.0% (4,309/4,309) | 100.0% (14/14) | 100.0% vs 100.0% (EQUAL)
Extracted Payload | 3,267,305 bytes | 1,958,826 bytes | 8,764 bytes | Delta: -1,308,479 B (-40.05%)
Windowing Scheme | 91 win (w=200 pkts) | 87 win (w=50 frames) | 5 win (w=3 PDUs) | 91 win vs 87 win
F1 Health Score | 100.00 / 100 (HEALTHY) | 100.00 / 100 (HEALTHY) | 100.00 / 100 (HEALTHY) | 100.00 vs 100.00 (COMPARABLE)
F2 Anomaly Windows | 5 [1, 2, 12, 88, 90] | 5 [0, 83, 84, 85, 86] | 1 [4] | 9 metrics NOT_COMPARABLE
Peak Anomaly Score | 0.8576 (Window 90) | 0.7406 (Window 86) | 0.5018 (Window 4) | Format-specific models
Dominant Feature | PID 256 (98.5% share) | Modal DFL 8304b (92%) | GSE_EXT_NPA (100%) | Structural metrics barred
Shannon Entropy | 0.1361 bits | N/A (Continuous DFL) | 0.0000 bits | NOT_COMPARABLE
Reconciled Ground Truth: All numbers match the authoritative ground truth ledger. Peak BBFrame anomaly score 0.7406 reconciled.

## Slide 22: GSE CAPTURE INGESTION & DECODING DETAILS
Authoritative GSE Capture File: 01_RAW_DATA/02_GSE/GSExtract/sample.ts (File size: 9,324 bytes).
Observed Decoded PDUs: 14 variable-length GSE Protocol Data Units (PDUs) extracted and validated.
GSE Length Field Specification: 12-bit header length field (Valid range: 0–4095 bytes payload).
Theoretical Maximum PDU Size: 4097 bytes including the 2-byte base header.
Observed Maximum PDU Size: 1,444 bytes observed in the sample capture stream.
Format Auto-Sniffing Handling: File extension .ts retained natively; multi-tier format sniffer correctly identifies GSE PDU content without requiring file renaming to .gse.

## Slide 23: TESTING AND VALIDATION FRAMEWORK
Total Test Suite Validation Result: 240 / 240 Passing Tests (100% Pass Rate across the entire application).
207 Backend Unit Tests: 11 dedicated test modules executing under Python's native unittest framework in 8.710 seconds:
• test_ts_parser (20 tests): 188B packet parsing, sync recovery, PID filtering, CC checking, TEI detection
• test_gse_parser (18 tests): Variable PDU lengths, S/E fragmentation flags, LT types, EtherType extraction
• test_bbframe_parser (23 tests): 10B BBHeader parsing, MATYPE flags, UPL/DFL, table-driven CRC-8 verification
• test_stream_handler & features (24 tests): Multi-tier format sniffing, unified metric extraction, Shannon entropy
• test_health, anomaly & patterns (48 tests): Priority-1 health penalties, Isolation Forest calibration, transition filtering
• test_timeline, explanation, comparison, report (74 tests): Byte offset tracking, signed Z-scores, semantic audit, multi-format renderers
33 Frontend Component Tests: 33 UI tests verifying interactive timeline controls, dashboard rendering, and export state.

## Slide 24: TECHNOLOGIES & ENGINEERING STACK
Backend Analytics & AI Core
Programming Language: Python 3.x (Core implementation)
Scientific Computing: NumPy (>=1.26), SciPy (>=1.11), Pandas (>=2.1)
Machine Learning Engine: scikit-learn (Isolation Forest anomaly model)
Testing Framework: Python unittest, pytest (>=7.4), pytest-cov
Visualization, UI & Tooling
Visualization Engines: Matplotlib (>=3.8), Plotly, HTML5, CSS3
Reporting Generators: JSON, GitHub-Flavored Markdown, ASCII Text, Standalone HTML5
IDE & Version Control: VS Code, Git, GitHub Repository
Operating System: Cross-platform support (Windows / Linux)

## Slide 25: INDIVIDUAL CONTRIBUTIONS & RESPONSIBILITIES
Team Member Name | University Roll No. | Project Role | Technical Responsibilities & Completed Modules
Sk Samad | 20231COM0031 | Testing, Validation & Documentation Lead | Automated test suite execution (207 backend / 33 frontend tests), technical documentation authoring, literature review synthesis, experimental report verification.
Y Vengala Rao | 20231COM0001 | Frontend, Visualization & Development | Frontend UI MVP development, interactive timeline chart components, dashboard layout design, presentation slide deck authoring.
C Rakeshwar | 20231COM0008 | Core Development & Technical Lead | Backend architecture, multi-format stream parsers (TS/GSE/BBFrame), F1–F7 analysis engines, AI/ML Isolation Forest model integration, system integration.
Equal Team Contribution: All team members actively contributed to development, verification, and documentation under guide supervision.

## Slide 26: GITHUB REPOSITORY ACCESS
Public Repository Access: The official PRJ_111 source code, test suite, and documentation are hosted with full public access permission.
Repository URL: https://github.com/rakesh0709/PRJ_111_DVB-S2_Analysis.git
Repository Contents: Complete F1–F7 implementation, 207 backend unit tests, 5 real-data experiment scripts, documentation ledgers, and standalone report renderers.
Branching & Maintenance: Active development branch maintained under git version control with comprehensive commit history.
Scan QR code to access public GitHub repository

## Slide 27: OPERATIONAL LIMITATIONS
Absence of Physical RF Telemetry: Operating on post-demodulator digital output, the software cannot directly measure physical RF carrier parameters (SNR, MER, C/N, carrier offset, or LNB drift).
Offline File Capture Focus: Processes pre-recorded stream captures (.ts, .pcap, .bin); live Software-Defined Radio (SDR) hardware streaming is not currently integrated.
Scarcity of Public Labeled Ground Truth: The absence of standardized, frame-labeled satellite fault benchmarks requires unsupervised Isolation Forest modeling rather than supervised classification.
Format-Specific Header Parsing Scope: Relies on standardized structural headers (BBHeader, GSE PDU, TS 188B); proprietary unencapsulated payloads require format adapters.

## Slide 28: FUTURE WORK ROADMAP
Full PSI/SI Table Parsing: Implement full Program Association Table (PAT), Program Map Table (PMT), and Service Information decoders resolving elementary audio/video codecs (AVC/H.264, HEVC, AC-3).
Physical RF Cross-Correlation: Ingest external demodulator telemetry logs (SNR/AGC) for cross-layer correlation between physical link budget and digital stream health.
Deep Learning Model Extensions: Integrate semi-supervised Autoencoders and LSTM networks trained on synthetic fault injection benchmarks.
Real-Time SDR Streaming Integration: Support real-time circular buffer streaming directly from GNU Radio or USRP SDR hardware tuners.

## Slide 29: CONCLUSION
Unified Multi-Format Solution: Successfully developed a software application for analysis and processing of DVB-S2 receiver output streams across MPEG-TS, GSE, and BBFrame formats.
Comprehensive Feature Implementation: Features F1 through F7 are 100% implemented, audited, and verified with an automated test suite achieving 240 / 240 passing tests (100% pass rate).
Rigorous Engineering & Epistemic Guard: Enforced a semantic cross-format audit preventing invalid metric comparisons, bounded signed Z-score diagnostic attributions, and strict domain-safety guards.
Validated Operational Readiness: Empirically validated against real satellite broadcast captures and deployed automated multi-format report renderers for operator decision support.

## Slide 30: REFERENCES (IEEE FORMAT)
[1] A. Morello and V. Mignone: DVB-S2: The Second Generation Standard for Satellite Broad-Band Services, Proc. IEEE, vol. 94, no. 1, pp. 210–227, 2006.
[2] G. Albertazzi et al.: On the Adaptive DVB-S2 Physical Layer: Design and Performance, IEEE Wireless Commun., vol. 12, no. 6, pp. 62–68, 2005.
[3] E. Casini et al.: DVB-S2 Modem Algorithms Design and Performance over Typical Satellite Channels, Int. J. Satell. Commun. Netw., vol. 22, no. 3, pp. 281–318, 2004.
[4] J. Cantillo et al.: GSE: A Flexible, Yet Efficient, Encapsulation for IP over DVB-S2 Continuous Generic Streams, Int. J. Satell. Commun. Netw., vol. 26, pp. 231–250, 2008.
[5] J. Cantillo et al.: Design Issues for Generic Stream Encapsulation (GSE) over DVB-S2, in Proc. IWSSC, 2007, pp. 276–280.
[6] P. Th. Savvopoulos et al.: A Software-Radio Test-bed for DVB-S2 Receiver Performance, in Proc. SPSC, 2008.
[7] K. Hundman et al.: Detecting Spacecraft Anomalies Using LSTMs and Nonparametric Dynamic Thresholding, in Proc. ACM KDD, 2018, pp. 387–395.
[8] E. Arbon et al.: Anomaly Detection in Satellite Communications Systems using LSTM Networks, in Proc. MilCIS, IEEE, 2018.
[9] D. Pan et al.: Satellite Telemetry Data Anomaly Detection Using Bi-LSTM Prediction Based Model, in Proc. IEEE I2MTC, 2020.
[10] Z. Zeng et al.: Satellite Telemetry Data Anomaly Detection Using Causal Network and Feature-Attention-Based LSTM, IEEE Trans. Instrum. Meas., vol. 71, 2022.

## Slide 31: THANK YOU / QUESTIONS & DEFENSE
Project Identifier: PRJ_111
Project Full Title: Development of a Software Application for Analysis and Processing of DVB-S2 Receiver Output Stream
Academic Milestone: CSE7102 – Mini Project (Review-2 Milestone | 26-09-2026)
Supervising Guide: Asst. Prof. Irfan Rajab Bhat
Department & School: Department of Computer Science and Engineering, Presidency School of Computer Science and Engineering, Presidency University, Bengaluru
Open for Questions: We welcome feedback, technical questions, and defense evaluation from the review panel.